OWNERS MANUAL

HIGH & DRY BOATLIFTS (Pty) Ltd

239 Broadlands Rd

Strand, Western Cape

South Africa

Ph +27 (0)823800027

INDEX

- Introduction

- Operating Instructions

  - Raising your boat

  - Launching your boat

- Do’s and don’ts

- Mooring Locations

- Maintenance

- Technical Specification

- Product Installation and use warning disclaimer

- Warranty Certificate

1.  INTRODUCTION

Welcome to High & Dry Boatlifts dry storage solution.

High & Dry Boatlift is a patented, designed and engineered dry boat storage solution aimed at making dry boat storage affordable and user friendly so everyone can use it.

The protection and piece of mind it offers you are unrivalled in the industry. It’s unique launching and lifting mechanism enables you to leave your float unattended for long periods of time.

High & Dry Boatlifts ensures:

- You have less marine growth on your boat, eliminating anti-fouling and thus better fuel consumption and speed.

- You can launch and retreive your boats in seconds so no more spending time launching boats on trailers when you could be on the water.

- Galvanic corrosion is a thing of the past leading to longer engine life.

- Increased resale value of your boat.

- Reduced maintenance time and cost on your boat.

2.  OPERATING INSTRUCTIONS

2.1 RAISING YOUR BOAT

- Position boat over lift and attach guide ropes to rear cleats of the boat.

(For first time installation position the boat’s center of gravity more or less in the middle of the boat. Start the blowers. The float must lift horizontally. If the bow rises bow first, switch of blowers and let the lift sink back into the water. Move boat fwd and try again until the lift lifts horizontally. If the stern lifts first, move the boat back until the lift lifts your boat horizontally. This may take a few iterations.)

- Attach the hose pipes to the upper hose connectors on the Blower House (top four connectors)

- Switch on all four blower switches

- Once bubbles appears under all four float compartments, switch off all blowers

- Ensure the minimum waterline stripe is above the water and the float remains stationary in a horizontal position.

- Attach mooring line

2.2   TO LAUNCH BOAT

- Detach mooring line.

- Always blow the air through the system until bubbles appear under all compartments to ensure there are now blockages and that all pumps are supplying enough pressure.

- Attach hose pipes to the “BOTTOM” attachments of  Blower House (bottom four connectors)

- Switch on all four blowers

- Once the float have submerged to under the white gelcoat line, switch off blowers. (approx 15 seconds)

3. DO’S and DON’TS

Do

DO ensure that your electrical supply conforms to regulations at the Marina. Please ensure that safety is your first priority, you are working with electrical equipment and as such have to be cautious.

DO always use guide ropes, they are required for proper positioning of the boat and if not used in the operating of the Boatlift, High & Dry Boatlift   (Pty) Ltd accepts no responsibility for any damage or injury caused whatsoever.

Do always raise the float if not used for a period of time or in severe weather or surge conditions.

Do secure the boat to the dock in case the lift is lowered in you absence.

Don’t

DON’T allow anyone on the boat during the lifting or launching operation.

DON’T leave the blowers running when launching the boat.

DON’T attempt to raise any other boat accept the one it was adjusted for. (Your dealer can

adjust the float for any other boat).

4. MOORING LOCATIONS

CAUTION

High winds and rough water conditions.

The boat float is not designed to withstand severe water or wind conditions. Should the potential of severe conditions exist it is recommended that the mooring lines be secured from dock structure to bow and stern cleats of the craft to avoid damage to the Boatlift mooring apparatus.

CAUTION

If the lift is left in the fully submerged position damage to the lift and dock may occur during severe weather conditions or high surges. Raise the lift to ride out severe weather conditions and surges.

Suggested mooring layout diagrams

Cross tie front two mooring lines

5.  MAINTENANCE

There are no moving parts on the lift so maintenance is minimal.

It is recommended to brush off any marine growth with a nylon brush once a year by raising the float without the boat.

In areas with prolific marine growth the “Blow hole” needs to be cleared of marine growth as required from time to time. Use a nylon brush to remove any marine organisms.  The Blow hole is the air and water inlet/ outlet situated on the bottom of each pontoon chamber.

6. TECHNICAL SPECIFICATION

| HIGH & DRY BOATLIFT - SPECIFICATION |
| --- |
| Lift Capacity (kg) | Total Float Length | Min Boat Length | Max Boat Length | Draft |
| 1000 kg | 4m | 3m | 5.1m/17ft | 600mm |
| 1400 kg | 5.5m | 4m | 6.5m/ 21ft | 600mm |
| 1900 kg | 5.5m | 4m | 6.5m/21ft | 900mm |
| 2300 kg | 6.5m | 5m | 7m/24ft | 900mm |
| 2800 kg | 6m | 5m | 7m/24ft | 1200mm |
| 3200 kg | 7m | 5.5m | 8.5m/28ft | 1200mm |
| 4200 kg | 7m | 5.5m | 8.5/28ft | 1400mm |
| 5000 kg | 8m | 6.5m | 9.75/32ft | 1400mm |
| 5500 kg | 9m | 7.5m | 10.5/34ft | 1800mm |
| 6000 kg | 10m | 8.5m | 11.5/38ft | 1800mm |
| 7500 kg | 10m | 8.5m | 11.5/38ft | 2000mm |

**Beam adjusted to suit boat model.

7. PRODUCT INSTALLATION AND USE WARNING DISCLAIMER

Assembly, installation and repairs to a boatlift should only be carried out by an authorized boatlift technician. If performed by any other person, other than a trained and approved High & Dry Boatlift Technician, all warranty’s are void and High & Dry Boatlift (Pty) Ltd take no responsibility for any damage caused whatsoever.

The contents of this manual are subject to change without notice and should not be construed as a commitment, presentation, warranty or guarantee of any method, product or device by High & Dry Boatlift (Pty) Ltd.

Whilst High & Dry Boatlift (Pty) Ltd has made every effort to ensure the accuracy and completeness of the

information and material contained herein, neither it nor its data providers give any warranty or guarantee

concerning the accuracy or completeness of the information hereby provided, and disclaims any

liability arising from the use of this document.

High & Dry Boatlift (Pty) Ltd reserves the right to replace any failed components of the boat lift device at their sole discretion.

High and Dry warranty does not include damages to yourself, boat or equipment under any circumstances.

The obligations and liabilities of High & Dry Boatlift (Pty) Ltd are limited to those of the High & Dry Boat lift device only.

The warranty is not transferrable and applies solely to the first purchaser of the High & Dry Boatlift.

8. WARRENTY CERTIFICATE

The Boatlift   provides the following warranty for its boat storage device.

- Workmanship and construction – 12 months

- Hoses, ropes and fasteners – 12 months

- Air blowers (original supply) – 12 months

- GRP Pontoons – 24 months

Warranty is void if:

- The Boatlift   is used for any other purpose than private boat Storage.

- Total all up weight of the supported vessel including live load exceeds that of the specification of the Boatlift.

- Modifications have been made to the device or any parts thereof.

- The device is allowed to ‘Bottom out’ on the sea floor.

- The device is used in a ‘rough water’ site.

- Willful damage or vandalism.

- The device is left in the water to freeze.

WARRANTY CERTIFICATE

This warranty certificate is issued to __________________________________________

Mooring address __________________________________________________________

This is to certify that the Boatlift designated________________________(serial no)

is warranted by  High & Dry Boatlifts under the terms and conditions stipulated in this manual

Serial Number______________________________

Vessel Details____________________________(Brand, Model, Size)

Installed by ________________________________ (service agent)

Date Installed_______________________________

Please present this certificate to your dealer when presenting a claim.